## Slide 1
User (PC/Another FPGA etc)
FPGA
Register File
QSPI Controller
QSPI Flash Mem Real component
Clock
DQ0
DQ1
DQ2
DQ3
CS
Send Nonvolatile Data
Send Quad command
Send Quad Address
Send Quad Data
State machines
Read data

## Slide 2
TB
TB process
FPGA
Register File
QSPI Controller
QSPI Flash Virtual component
Send Quad command
Clock
DQ0
DQ1
DQ2
DQ3
CS
Send Quad Address
Send Quad Data
State machines
Send Nonvolatile Data
Read data

## Slide 3
Reg name | Reg address | Reg Description | Reg initial Value
Data write | 0x00 | Bits(31:0) – Data Write to the QSPI flash memory | 0x00000000
Data read | 0x04 | Bits(31:0) – Data Read from the QSPI flash memory | 0x00000000
Address data | 0x08 | Bits(31:24) – NA Bits(23:0) – The address of the QSPI flash | 0x00000000
Command data | 0x0C | Bits(31:8) – NA Bits(7:0) – Command Data | 0x00000000
Send data | 0x10 | Bits 31:1 – NA Bit 0- ‘1’ – Send data to Flash memory ‘0’- Idle | 0x00000000
Registers File:

## Slide 4
Main State machine:
initial
Send_data(0) = ‘1’ and initialization state machine done = ‘1’
Read command
Data Register
Reset = ‘1’
Send_data(0) = ‘0’
Read status register
Command = 06h
Write enabled
Command = 05h or 70h
Fast Read
Command = 0Bh
Read command
Data Register
Send_data(0) = ‘1’
Send_data(0) = ‘0’
Sector Erase
Command = D8h
Write 8 bits command
Command = 81h or 61h
Write 16 bits command
Write Data to the QSPI
Command = B1h
Command = 02h
Done writing
Done writing
Done writing
Done writing
Done reading
Done reading

## Slide 5
Initialization State machine:
initial
Reset = ‘1’
Send command 06h(enable write) on single SPI
Reset = ‘0’
Send command B1h(write non vol.reg) on single SPI
Done sending command= ‘1’
Done sending command= ‘1’
Send 16 Bit Data F7AFh on single SPI
Done sending data = ‘1’
else
else
else
Done
Done sending data = ‘1’

## Slide 6
Read status register state machine:
initial
Main state machine = Read Status register
Initiate Send Quad command process
Reset = ‘1’
Main state machine != Read Status register
Initiate Read data process
Send Quad command process done = ‘1’
Write the Data to the Data Read Register
Read data process done = ‘1’
else
else
Notes: No dummy cycles when reading status registers

## Slide 7
Fast Read state machine:
initial
Main state machine = Fast Read
Read Address data Register
Reset = ‘1’
Main state machine != Fast Read
Initiate Send Quad command process
Initiate Send Quad Address
process
Send Quad Address
process done = ‘1’
Wait 10 dummy cycles
Read data process done = ‘1’
Write the Data to the Read Register
Dummy cycles done = ‘1’
else
else
else
else
Initiate Read data
process
Send Quad command process done = ‘1’
Done reading Registers file = ‘1’

## Slide 8
Write Data to the QSPI
state machine:
initial
Main state machine = Write data to QSPI
Read Address data and Data Write Registers
Reset = ‘1’
Main state machine != Write data to QSPI
Initiate Send Quad command process
Done reading Registers file = ‘1’
Send Quad Address
process done = ‘1’
Initiate Send Quad Data
process
Send Quad Data
process done = ‘1’
else
else
else
Initiate Send Quad Address
process
Send Quad command process done = ‘1’
else

## Slide 9
Sector Erase state machine:
initial
Main state machine = Sector erase
Read Address data Registers
Reset = ‘1’
Main state machine != Sector erase
Initiate Send Quad command process
Done reading Registers file = ‘1’
Send Quad Address
process done = ‘1’
else
else
Initiate Send Quad Address
process
Send Quad command process done = ‘1’
else

## Slide 10
Write 8 bits command state machine:
initial
Main state machine = Write 8 bits command
Initiate Send Quad command process
Reset = ‘1’
Main state machine != Write 8 bits command
Send Quad command process done = ‘1’
else
Initiate Send Quad Data
process
else
Send Quad Data
process done = ‘1’

## Slide 11
Write 16 bits command state machine:
initial
Main state machine = Write 16 bits command
Initiate Send Quad command process
Reset = ‘1’
Main state machine != Write 16 bits command
Send Quad command process done = ‘1’
else
Notes: LSB sending first, see example for writing FEF8h to the non volatile register :
F8
FE
LSByte
MSByte
Data sending direction…
Initiate Send nonvolatile data
process
else
Send Quad Data
process done = ‘1’